Geologic computing Hw 4
Steven Rizo

Problem 1:
Determining the frequency-magnitude relationship for a given earthquake catalog. This will count and output the number of earthquakes greater than or equal to each magnitude from M2 to M9 and the log of each frequency.

Command:
perl magnitude.pl earthquake_catalog_example.dat > magnitude.out
or
perl magnitude_hash.pl earthquake_catalog_example.dat > magnitude_hash.out

Output:
Number of events by Richter Magnitude
M2 = 21500
M3 = 15720
M4 = 2432
M5 = 377
M6 = 35
M7 = 6
M8 = 0
M9 = 0

Log number of events by Richter Magnitude
M2 = 4.3324384599156
M3 = 4.19645254170339
M4 = 3.3859635706007
M5 = 2.57634135020579
M6 = 1.54406804435028
M7 = 0.778151250383644
M8 = -inf
M9 = -inf

Discussion:
Considering the Gutenburg-Richter Law states that there is supposed to be a linear correlation between the magnitude and the log of the frequency, this data seems to support the law. It can be seen with a nearly 1 to 1 change between magnitude and log-frequency from M3 to M7. The problem with this is that the change from M2 to M3 does not fit the law. An explanation for this could be that there are smaller events within the M2 category that were not included or recorded in this dataset, so that the value is lower than what would actually be seen. The values for M8 and M9 are only because there were no events of this magnitude, so this doesn’t contradict the Gutenburg-Richter Law.Problem 1 Flowchart:
Begin

Input: earthquake catalog data
Initialize: hash for M2 to M9 variables

Read line of data and assign variables

If magnitude >= N

Increase counter for M(N)
For each value of magnitude N from 2 to 9

More values for N?

More data?

False
True
True
False

False
True

Output: print values for number of
earthquakes by magnitude
End

Problem 2:
This problem uses the script developed in problem 1 and applies it to a selected area of USGS data. I initially looked at data just in the Lassen region, but there was limited data. I then included more of Northern California and a bit of data off of the coast near the triple junction. I will also be using data from Japan to see values for some of the larger magnitude earthquakes. Both data sets include events magnitude 2 and above from January 1, 2000 to present.

Commands:
perl magnitude_csv.pl north_cal.csv > magnitude_cal.out
and
perl magnitude_csv.pl japan.csv > magnitude_japan.out

Outputs:
Northern California
Number of events by Richter Magnitude
M2 = 17108
M3 = 1491
M4 = 226
M5 = 29
M6 = 3
M7 = 0
M8 = 0
M9 = 0

Log number of events by Richter Magnitude
M2 = 4.23319924158477
M3 = 3.17347764345299
M4 = 2.3541084391474
M5 = 1.46239799789896
M6 = 0.477121254719662
M7 = -inf
M8 = -inf
M9 = -inf
Japan
Number of events by Richter Magnitude
M2 = 16841
M3 = 16840
M4 = 15408
M5 = 1966
M6 = 207
M7 = 21
M8 = 2
M9 = 1

Log number of events by Richter Magnitude
M2 = 4.22636787585649
M3 = 4.22634208716363
M4 = 4.18774626978046
M5 = 3.29358351349612
M6 = 2.31597034545692
M7 = 1.32221929473392
M8 = 0.301029995663981
M9 = 0

Discussion:
While lacking in larger magnitude earthquakes, the data from Northern California has a very consistent 1 log-frequency to 1 magnitude ratio. This shows a very clear example of the Gutenburg-Richter Law with a linear relationship between the log of the number of events and the magnitude. In contrast, the data from Japan seems to be heavily weighted towards higher magnitude events. The fact that the values for M2, M3 and M4 are all within 1000 events shows a main reason, as this indicates that there is little data for earthquakes below M4 from this database. This explains the plateau in log-frequency for M2 to M4. However, starting from M4 up to M8 displays a fairly consistent Gutenburg-Richter relationship with linear relation as seen before. The small change from M8 to M9 is likely due to the rarity of these data values, and results from the specific beginning and end time for the dataset. Overall, the Gutenburg-Richter relationship can be seen throughout the data sets from different regions.